## Slide 1
P300 EEG-Based BCI
Cross-Subject Classification Pipeline
v1 → v3 → v4 → Threshold Calibration
M.Tech Project | Department of AI & Data Science
2025 – 2026
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 2
What is P300?
An ERP component used as a brain–computer interface signal
The P300 Signal
The P300 is a positive EEG deflection ~300 ms after a rare, attended stimulus.
In a P300 Speller:
• A 6×6 letter matrix flashes rows and columns
• The row/column containing the target letter evokes P300
• Non-target flashes produce no P300
Key properties:
• Latency: 200–500 ms post-stimulus
• Amplitude: 5–10 µV above baseline
• Maximal at Pz (central-parietal)
• Highly variable across subjects
Dataset (BCI Competition II, DS II)
8 subjects, 8 EEG channels, 250 Hz
Epoch window: −200 ms to +800 ms
Total epochs: 33,489
TARGET epochs (y = 1)
5,575
16.65% — P300-evoking
NON-TARGET (y = 0)
27,914
83.35% — frequent flashes
⚠ 83:17 class imbalance — accuracy alone is misleading. Use Balanced Accuracy, ROC-AUC, and PR-AUC.
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 3
Pipeline Overview
Four versions built progressively to tackle cross-subject generalisation
PREPROCESS
0.1–30 Hz bandpass Common Average Ref Epoch: −200 to +800 ms
→
FEATURES
Crop 200–500 ms Bin average (5 ms) 120-dim or Riemannian
→
CLASSIFY
rLDA / SVC Stratified 5-Fold WS LOSO cross-subject
→
CALIBRATE
Youden's J threshold 10% held-out val Fix BAcc collapse
v1
Raw bins 120-dim rLDA
v3
xDAWN sweep k=0,2,4,6
v4
Riemannian EA + TS + rLDA
v4+cal
Youden's J calibration
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 4
Critical Finding: Label Inversion Bug
Original code assigned y=1 to NON-TARGET — silently flipped all learning
flash[:, 3] encodes: 1 = NON-TARGET (frequent, 83%) 2 = TARGET (P300-evoking, 17%)
Original code used flash[i,3] == 1 as the positive class — the model was learning to detect NON-targets.
BEFORE (wrong)
labels.append(
1 if flash[i, 3] == 1 else 0
)
→ y=1 assigned to NON-TARGET (83%)
AFTER (correct)
labels.append(
1 if flash[i, 3] == 2 else 0
)
→ y=1 assigned to TARGET (17%)
Why it was hard to catch:
• WS accuracy looked high (~85%) because the model just predicted the majority class
• AUC can flip: AUC(wrong direction) = 1 − AUC(correct direction)
• LOSO BAcc ≈ 0.51 near chance — the real signal was invisible
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 5
v1: Baseline — Raw Binned ERP Features
Simple, interpretable; establishes the within-subject vs cross-subject gap
Filter 0.1–40 Hz
→
Epoch −200→+800ms
→
Crop 200–500ms
→
Bin avg 5 ms bins
→
Flatten 120-dim
→
rLDA / SVC
Within-Subject (5-Fold Stratified CV)
Balanced Accuracy
0.612
ROC-AUC
0.762
P300 signal
DETECTED
within-subject
Cross-Subject (Leave-One-Subject-Out)
Balanced Accuracy
0.519
≈ chance (0.500)
ROC-AUC
0.636
Cross-subject gap
LARGE
BAcc drops 9.3pp
Why LOSO fails
• ERP latency varies ±50 ms across subjects
• Amplitude scale differs 3–5×
• P300 topography shifts with head shape
• Threshold (0.5) from training subject
does not transfer to test subject
→ Need geometry-aware features
→ Need calibrated threshold
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 6
v3: xDAWN Spatial Filter Sweep (k = 0, 2, 4, 6)
Does a subject-trained spatial filter improve cross-subject generalisation?
k
Feat dim
WS BAcc
WS AUC
LOSO BAcc
LOSO AUC
0
120
0.591
0.742
0.509
0.607
2
30
0.558
0.719
0.505
0.606
4
60
0.581
0.732
0.507
0.608
6
90
0.589
0.740
0.509
0.605
Finding: xDAWN does NOT improve LOSO regardless of k — all LOSO AUC ≈ 0.606±0.001
Reason: With only 8 EEG channels, the spatial filter learned on 7 training subjects does not capture the test subject's unique P300 topography. The information bottleneck is topology, not feature dimension.
→ Next step: model the geometry of the covariance space (Riemannian pipeline)
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 7
v4: Riemannian Covariance Pipeline
XdawnCovariances → Euclidean Alignment → Tangent Space → rLDA
XdawnCov (nfilter=4)
Augmented (2nf+1)×(2nf+1) SPD matrices
→
Euclidean Alignment
Whiten by train mean cov R⁻¹/² C R⁻¹/²
→
Tangent Space
Map SPD → Euclidean 45-dim vector
→
rLDA
Regularised Linear Discriminant
nfilter Sweep Results (rLDA)
nf
TS dim
WS BAcc
WS AUC
LOSO BAcc
LOSO AUC
LOSO PR-AUC
1
6
0.506
0.582
0.500
0.552
0.203
2
15
0.550
0.673
0.504
0.602
0.243
4
45
0.600
0.746
0.517
0.648
0.296
nf=4 best: LOSO AUC 0.636 → 0.648 (+1.2pp) PR-AUC = 0.296 = 1.78× above random (0.167)
Riemannian geometry improves ranking — but LOSO BAcc still 0.517 because threshold does not transfer.
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 8
Threshold Calibration: Youden's J
The AUC is good — the default threshold just doesn't transfer across subjects
Why Default Threshold Fails
Default threshold = 0.5 works when train and
test score distributions are aligned.
In LOSO:
• Training subjects define one score scale
• Test subject has a different scale
• Threshold 0.5 is no longer the optimal cut
• BAcc collapses to ~0.50 even when AUC > 0.60
Solution: Youden's J
thresh* = argmax(TPR − FPR) on ROC curve
Fitted on a 10% held-out val split of
the training subjects per LOSO fold.
Calibration Procedure (per LOSO fold)
1. Split training subjects:
90% → fit Riemannian pipeline + rLDA
10% → find Youden's J threshold
2. Re-fit final model on 100% of training
subjects (no data wasted)
3. Apply calibrated threshold to
held-out test subject
4. Report BAcc at calibrated threshold
(AUC unchanged — still threshold-free)
Per-Subject Calibrated LOSO Results (nf=4, rLDA)
Subj
thresh
BAcc
AUC
S01
0.178
0.510
0.539
S02
0.165
0.567
0.593
S03
0.174
0.581
0.611
S04
0.181
0.616
0.667
S05
0.165
0.628
0.684
S06
0.154
0.621
0.668
S07
0.183
0.690
0.750
S08
0.156
0.627
0.672
Calibrated BAcc
0.605
vs 0.517 uncalib
ROC-AUC
0.648
unchanged
PR-AUC
0.296
1.78× random
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 9
Results Summary — All Versions
Progressive improvement from raw features to calibrated Riemannian pipeline
Version
Method
Eval
BAcc
ROC-AUC
PR-AUC
Notes
v1
rLDA 120d raw
WS
0.612
0.762
—
Strong within-subject
v1
rLDA 120d raw
LOSO
0.519
0.636
—
Near-chance BAcc
v3 k=0
rLDA 120d CAR
LOSO
0.509
0.607
—
CAR/filter gives no LOSO gain
v3 k=6
rLDA+xDAWN(6)
LOSO
0.509
0.605
—
xDAWN does not help LOSO
v4 nf=4
Riem EA+TS rLDA
WS
0.600
0.746
0.443
Best WS after v1
v4 nf=4
Riem EA+TS rLDA
LOSO
0.517
0.648
0.296
Best AUC, threshold issue
v4+cal
Riem+Youden's J
LOSO
0.605
0.648
0.296
BEST cross-subject system ★
Random baselines: BAcc=0.500 AUC=0.500 PR-AUC=0.167 (= prevalence 16.65%)
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 10
Why These Metrics?
Accuracy is misleading under 83:17 imbalance — three complementary metrics used
Balanced Accuracy (BAcc)
= (TPR + TNR) / 2 Equal weight to both classes. Random baseline = 0.500. Our best = 0.605.
Measures threshold performance fairly.
ROC-AUC
Area under ROC curve. Threshold-free ranking metric. Random baseline = 0.500. Our best LOSO = 0.648.
Does the model rank targets above non-targets?
PR-AUC (Avg Precision)
Area under Precision-Recall. Sensitive to minority class. Random baseline = prevalence = 0.1665. Our best = 0.296 (1.78×).
Most honest metric under severe imbalance.
All three metrics are reported — they measure different aspects of the same classifier.
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 11
Conclusions & Future Work
Conclusions
1. Label sanity check is critical
flash[:,3]==2 is TARGET; original code had it inverted.
2. Within-subject P300 is detectable
v1 rLDA: WS BAcc=0.612, AUC=0.762
3. xDAWN does not help cross-subject
8-channel spatial filter doesn't transfer (v3 sweep).
4. Riemannian geometry improves ranking
LOSO AUC: 0.636 → 0.648 with EA + TangentSpace.
5. Threshold calibration recovers BAcc
Youden's J: BAcc 0.517 → 0.605 (+8.8 pp)
Best system: v4 nf=4 + Youden's J
LOSO BAcc=0.605 AUC=0.648 PR=0.296 (1.78× chance)
Future Work
Short term:
• Sweep nfilter to 6, 8
• Try MDM (Minimum Distance to Mean)
as Riemannian classifier
• Platt scaling as alternative calibration
Medium term:
• Riemannian alignment at test time
(online EA with sliding window)
• Subject-independent model fine-tuning
with minimal labelled test data (10 trials)
Long term:
• Deep learning: EEGNet, ShallowConvNet
• Transfer learning across datasets
• Real-time P300 speller evaluation
• More subjects / higher-density EEG
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 12
Dataset: P300 Speller — 8 Subjects
MATLAB .mat files, 250 Hz, 8 EEG channels, ~24 min recording per subject
Per-Subject Statistics
Subject
Epochs
Target
Non-target
Bad Chs
Threshold
S01
4200
700
3500
—
150 µV
S02
4198
700
3498
—
200 µV
S03
4197
700
3497
P4, PO8
100 µV
S04
4191
697
3494
PO8
100 µV
S05
4112
680
3432
Oz
100 µV
S06
4197
700
3497
—
150 µV
S07
4198
698
3500
—
150 µV
S08
4196
700
3496
—
150 µV
TOTAL 33,489 epochs 5,575 target (16.65%) 27,914 non-target (83.35%)
Raw .mat File Structure
scipy.io.loadmat('P300S01.mat')
mat['data']['X'] → (358372, 8)
Continuous EEG [samples × channels]
~24 min @ 250 Hz
mat['data']['flash'] → (21495, 4)
Col 0: onset sample index
Col 1: row/col ID (12 rows+cols in 6×6 grid)
Col 3: 1=NON-TARGET 2=TARGET ← key!
mat['Fs'] = 250 Hz
mat['Trials'] = 35 words
mat['Word'] = 'TOKENMIRARJUJU...'
mat['channelNames'] = [FZ,CZ,P3,PZ,P4,PO7,PO8,OZ]
EEG Channel Layout (8 channels, 10-20 system)
Frontal: Fz, Cz Parietal: P3, Pz, P4
Parieto-occipital: PO7, PO8 Occipital: Oz
→ Coverage chosen for P300 (max amplitude at Pz/Cz)
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 13
End-to-End Flow: Loading → Preprocessing → Features
Every transformation step with exact shapes and parameters
STEP 1 — Data Loading (scipy.io.loadmat)
P300S01.mat … P300S08.mat
mat = scipy.io.loadmat('P300S0X.mat')
X_raw = mat['data']['X'] # (358372, 8) continuous EEG µV
flash = mat['data']['flash'] # (21495, 4) stimulus event table
onset = flash[:, 0] # sample index of each flash
label = flash[:, 3] # 1=non-target 2=target
Output per subject:
X_raw : (N_samples, 8) raw continuous signal
flash : (N_flashes, 4) event markers
~21,500 flash events per subject
~358,000 raw samples (~24 min)
STEP 2 — Preprocessing (MNE-Python)
p300_preprocess_v2.py
2a
Bad channel interpolation
S03→P4,PO8 S04→PO8 S05→Oz Spherical spline interpolation from neighbours
2b
Bandpass filter
0.1 – 30 Hz (FIR, Hamming window) Removes DC drift + high-freq noise + muscle artefacts
2c
Common Average Reference
Each sample -= mean across all 8 channels Reduces global noise / electrode drift shared across channels
2d
Epoching
Onset ± window: −200 ms to +800 ms = 250 samples per epoch (X_raw[onset−50 : onset+200, :])
2e
Baseline correction
Subtract mean of pre-stimulus window [−200 to 0 ms] per channel Removes DC offset within each epoch
2f
Artifact rejection
Reject epoch if any sample > threshold (100–200 µV, subject-specific) S01 keeps ~4200, S05 most rejected (threshold 100 µV)
Shape after epoching: (n_epochs, 8, 250) → 33,489 epochs total across 8 subjects
STEP 3 — Feature Extraction (v1/v3 path)
extract_p300_features_v2.py
Crop P300 window
(n,8,250) →(n,8,75)
200–500ms samples 100:175
→
Bin averaging
(n,8,75) →(n,8,15)
15 bins × 5 samples each
→
Flatten
(n,8,15) →(n,120)
8 channels × 15 bins
→
Label assignment
flash[:,3]==2 → y=1 target
flash[:,3]==1 → y=0 non-tgt
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 14
End-to-End Flow: Classification → Evaluation
Two evaluation protocols: within-subject 5-fold CV and cross-subject LOSO
STEP 4 — v4 Riemannian Classification (inside each CV fold)
lda_svc_classifier_v4.py
XdawnCov (pyriemann)
(n,8,250) →(n,9,9)
nfilter=4 Fitted on train only (no leakage)
→
Euclidean Alignment
(n,9,9) →(n,9,9)
Whiten by train mean cov R⁻¹/² C R⁻¹/²
→
Tangent Space
(n,9,9) →(n,45)
Riemannian log at mean SPD n(n+1)/2 = 45
→
Standard Scaler
(n,45) →(n,45)
Zero mean Unit variance Fitted on train
→
rLDA / SVC
(n,45) →score
Shrinkage LDA or linear SVC predict_proba
STEP 5 — Evaluation Protocols
Within-Subject CV (WS)
StratifiedKFold(n_splits=5)
• Split each subject's epochs 80/20
• Train + test on SAME subject
• Measures: upper bound performance
• Stratified → preserves 16.7% ratio
• Metrics averaged across 5 folds
Leave-One-Subject-Out (LOSO)
LeaveOneGroupOut() — 8 folds
• Train on 7 subjects → Test on 1
• Each subject is test subject once
• Measures: cross-subject generalisation
• Hardest evaluation — no subject overlap
• Threshold calibrated via Youden's J (v4)
STEP 6 — Metrics Reported
BAcc
(TPR+TNR)/2
Fair under imbalance Random = 0.500
ROC-AUC
roc_auc_score (y, proba[:,1])
Threshold-free Random = 0.500
PR-AUC
average_precision _score
Minority-class sensitive Random = 0.167
F1
2·P·R/(P+R) on target class
Calibrated result only Low under imbalance
M.Tech Project | P300 EEG Classification | 2025-26

## Slide 15
Thank You
Questions?
Best WS
BAcc 0.612 AUC 0.762
Best LOSO AUC
0.648 (nf=4 Riem)
Calibrated LOSO
BAcc 0.605 AUC 0.648
PR-AUC lift
0.296 1.78× chance
M.Tech Project | P300 EEG-Based BCI | 2025–26